## Slide 1
Lecture 3
Analysis of DNA, RNA, and protein levels
CHEM 570, Fall 2017
Concepts in Chemical Biology

## Slide 2
Overview
As a generalization, a binary (YES/NO) answer is sufficient for DNA analysis, whereas for RNA and protein, LEVELS are needed.
Two types of question may be asked:
1. Is a (DNA, RNA, protein) PRESENT in the sample?
2. What is the LEVEL of a (DNA, RNA, protein) in the
sample?

## Slide 3
DNA is first cleaved by restriction enzymes, then...
Analysis of DNA by Southern blotting
Edwin Southern
Oxford University
Method to determine if a certain stretch of DNA is present
Southern blotting has largely been replaced by PCR analysis.

## Slide 5
Nitrocellulose
Synthesis:
First human created plastic (1862)
Sticky nature exploited to immobilize nucleic acids, as well as proteins

## Slide 6
Quantifying mRNA levels
mRNA is therefore isolated using a poly-T column:
Recall: mRNAs are generally polyadenylated
• rRNA, tRNA elute with high salt
• mRNA sticks to poly-T and elutes with low salt
mRNA is then quantified by:
• Northern blot
• rtPCR

## Slide 7
Quantifying mRNA by Northern blotting
Northern blotting is analogous to Southern blotting
• RNA is isolated and separated by electrophoresis
• Probing is done with a complementary DNA strand
• Typically the DNA strand is 32P-radiolabeled
• Fluorescent labels are also used

## Slide 8
Quantifying mRNA using PCR
rtPCR = reverse transcription / PCR
Most sensitive technique for mRNA quantification
Important to remember that PCR uses double stranded DNA as the template
Q: how do we go from mRNA to DNA?
Notes: Similar to PCR, except an extra enzyme, reverse transcriptase is used to convert mRNA into cDNA which can be read and used by taq polymerase as a template

## Slide 9
Reverse Transcriptase: mRNA  cDNA
A reverse transcriptase (RT) is an enzyme used to generate complementary DNA (cDNA) from an RNA template, a process termed reverse transcription
Enzyme mainly associated with retroviruses.
Some examples?

## Slide 10
animation: http://www.bio.davidson.edu/Courses/genomics/RTPCR/RT_PCR.html
One-pot procedure: add dNTPs, primers, and enzymes
Putting it together: rtPCR to quantify mRNA

## Slide 11
Utility (or not) of quantifying mRNA by rtPCR
• rtPCR uses PCR to amplify signal
• Detect low-abundance transcripts
• Ideal for end-point analysis: is mRNA present or not?
Dynamic range problem:
Various mRNA transcripts are present at levels that differ by several orders of magnitude
• At best, PCR and rtPCR are only semi-quantitative
• Amount of product correlates poorly with input DNA/RNA
PCR and rtPCR are good for binary “yes/no”
answers about the presence/absence of a DNA or RNA.
However, exact ratios of starting DNA/RNA CANNOT be
determined reliably using these methods.

## Slide 12
Nonlinear DNA amplification in PCR
plateau phase
The more template you begin with, the earlier you reach plateau phase
Monitoring amount
of DNA product
after each cycle
allows reliable quantification of amount of input DNA
Notes: At the beginning, there is a large excels of regents (nts) giving use an approximate doubling of DNA after each cycle
PCR product vs # of cycles
Log phase
Linear phase
Plateau phase

## Slide 13
“Real-time” PCR: Amount of DNA is quantified after each PCR cycle
• Signal generated in situ by use of fluorescent dye
• SYBR Green (see Slide 1-55) is commonly used
CT value =
# cycles to reach threshold
Real-time PCR machines can thermocycle and measure fluorescence simultaneously
Taqman ABI instrument
in Keck Center
Notes: rt = reverse transcription vs. real-time: in principle, can have rt-rtPCR, although not usually called that

## Slide 14
Real-time PCR with 10-fold dilutions of template
Note that all dilutions look similar in endpoint analysis
Threshold
Can be set to tell software where to take data but must be in the Log phase
Take a very concentrated sample and perform serial dilutions
Notes: Take a very concentrated sample and perform serial dilutions

## Slide 15
Real-time PCR with 10-fold dilutions of template
Set where the precision of the replicates is the highest
Notes: Some analogy here to initial-rate kinetics, versus fitting entire progress curve
Only data in the log phase is important for rt-PCR

## Slide 16
Real-time PCR: standard curve
With the standard curve, we can run our experimental sample and determine how much mRNA we had in the first place

## Slide 17
Can we determine if mRNA levels are altered in a certain tissue in response to a stimuli or in a certain disease?
Transcriptional (expression) profiling:
Simultaneous determination of levels of all RNA transcripts in a sample
Analysis of global RNA levels:
Transcriptional (expression) profiling

## Slide 18
Transcriptional profiling requires
DNA microarray technology
500 µm
Array: orderly arrangement of samples
Microarray: really small array (spots <200 µm diameter)
DNA microarray: Physically matches known and unknown oligonucleotides
A single experiment can provide information on thousands of transcripts (genes) simultaneously!

## Slide 19
Why use DNA microarrays?
1. Transcriptional (expression) profiling
• Global analysis of how a cell responds to a certain stimulus (e.g., drug or nutrient treatment, pH shift)
• Generally, protein levels are of major interest; however, Watson-Crick complementarity allows nucleic acids to be monitored easily
2. Genotype applications
• Direct analysis of DNA, including single-nucleotide polymorphisms (SNP detection)

## Slide 20
DNA
RNA
protein
translation
Reminder of Central Dogma
transcription
replication
If we want to examine the levels of all proteins in the cell, it is easier to look at the mRNAs.
Drawbacks?
Notes: Drawback: may not be precise correlation between mRNA and protein levels

## Slide 21
electrophoresis
of mRNA
transfer
mRNA on
nitrocellulose
incubate with
radiolabeled probe
visualize
What did we use before microarrays?
To determine the abundance of a single mRNA,
use Northern blotting (Slide 3-7)

## Slide 22
Cancer vs. normal
Heart vs. brain
Drug-treated vs. control
Changes in pH, nutrients,
toxins, temperature...
Equivalent to 10,000
simultaneous Northern
blots!
Overview of DNA microarrays
1
2
3
4
5
6

## Slide 23
A) Where does one get the DNA?
B) How does one make a microarray?
Overview of DNA microarrays
animation: http://www.bio.davidson.edu/courses/genomics/chip/chip.html
1. Grow cells; construct or purchase array

## Slide 24
2. Obtain mRNA from treated and non-treated cells
C) How is the mRNA isolated?
Note that everything in these experiments is relative.
Overview of DNA microarrays

## Slide 25
D) Why not use the mRNA directly?
E) How are the cDNA samples labeled?
mRNA cDNA
reverse
transcriptase
3. Reverse-transcribe mRNA ® cDNA, in labeled form
Overview of DNA microarrays

## Slide 26
4. Apply labeled cDNA samples to prefabricated DNA array
Overview of DNA microarrays

## Slide 27
F) How expensive is
this instrumentation?
G) Can I do these experiments here at Illinois?
5 & 6. Scan slides and analyze data
Overview of DNA microarrays

## Slide 28
A) Where does one get the DNA?
Nat. Biotechnol. 2004, 22, 418
There are several types of microarrays:
1. Immobilized cDNA
• Actual full-length gene
• PCR-amplified from appropriate vector
• Spotted onto poly-Lys slides
2. Immobilized oligonucleotides
• 40 to 80 nucleotides (nt) in length
• Can be synthesized on slides, or spotted onto slides
3. Hexamer-based “universal arrays”
• All possible 46 = 4096 DNA hexamers
• Obviates need for organism-specific probes

## Slide 29
B) How does one make a microarray?

## Slide 30
Robot will deliver ~1 nL/spot
Spots are 50–200 µm in size
>10,000 spots per slide
Microarraying robots

## Slide 31
C) How is the mRNA isolated?
• Most mRNAs have poly-A tail
• Isolated via poly-T column
• See Slide 3-6 for reminder
D) Why not use the mRNA directly?

## Slide 32
E) How are cDNA samples labeled?
mRNA cDNA
reverse
transcriptase
1) Incorporate fluorescent nucleotide conjugates during RT
• bulky substrates = less efficient incorporation
• expensive ($$$)
2) Incorporate functionalizable nucleotide during RT
• incorporate primary amino group (–NH2)
• modify after cDNA after RT with fluorophore

## Slide 33
Cy3
Cy5
Commonly used fluorophores: cyanine (Cy) dyes
excitation
emission

## Slide 34
Microarrayer = $50,000
Slide scanner = $50,000
The Keck center at Illinois has an arrayer.
They sell pre-made arrays, or you can bring cDNA
to them and they will make an array for you.
http://www.biotech.illinois.edu/centers/Keck/Functional_genomics/affymtx.htm
F) How expensive is this instrumentation?
G) Can I do these experiments at Illinois?

## Slide 35
Microarray analysis allowed grouping
of 203 cancer and normal lung samples...
Use of DNA arrays for cancer profiling
Bhattacharjee et al., Proc. Natl. Acad. Sci. USA 2001, 98, 13790
Garber et al., Proc. Natl. Acad. Sci. USA 2001, 98, 13784

## Slide 36
...and was predictive of therapeutic outcome
Bhattacharjee et al., Proc. Natl. Acad. Sci. USA 2001, 98, 13790
Garber et al., Proc. Natl. Acad. Sci. USA 2001, 98, 13784
Use of DNA arrays for cancer profiling

## Slide 37
Analysis of protein levels: Western blot
1
2
3
4

## Slide 38
1.
Chemiluminescence
Mechanism:
HRP-Antibody
Types of Antibodies used for visualization

## Slide 39
Other substrates that can generate light for detection
Types of Antibodies used for visualization

## Slide 40
2.
Atto dyes are a family of commercially available dyes with enhanced photophysical properties (e.g., high photostability)
Types of Antibodies used for visualization

## Slide 41
Coomassie staining (detects all proteins)
Immunoblot (Western blot)
(detects only the POI)
Analysis of protein levels: Western blot
Comparing two common procedures
for protein detection: